## Slide 1: WELCOME
Jordan Lake Water Supply Project Open House - Pittsboro
April 30, 2026

## Slide 2: Welcome!
We’re glad you’re here
Primarily open house format, with some information to highlight in a presentation format
Please sign in if you did not already
Sign up for our newsletter and emails!
Q&A time
Same presentation at 6:30 & 7:15
The Jordan Lake Water Supply Program Core Values are ...
Quality
Transparency
Public Engagement
Sustainability
Equity
Partnership
Notes: Inga for this slide then Jeff will begin with the next.

## Slide 3: Program Schedule
Planning & Permitting
2020-2025
Design & Preconstruction
2025-2027
Construction & Start-Up /Commissioning
2027-2032
WE ARE HERE
PDB Procurements
2025

## Slide 4: Water Intake and Treatment Plant
The Water Intake, Transmission Pipeline, and Water Treatment Plant are being designed to meet Partner needs through 2050 initially, and capable of being expanded to meet needs through 2070 and beyond.
A new raw water intake on the west side of Jordan Lake
A raw water supply pipeline and pump station to transport water from intake to treatment plant
A water treatment plant

## Slide 5: Program Updates
NEW Water Treatment Plant Location at 6903 Farrington Road
Adjacent to South Durham Water Reclamation Facility
Closer to City customers & existing City utility facilities
Opportunities for synergy & reduced costs
‘Seaforth Property’ in Chatham County, near Jordan Lake, will continue to be the site for the WIP Raw Water Pump Station
Design-Build teams selected for Intake/Raw Water Facilities & Water Treatment Plant projects – design is beginning soon
US Army Corps of Engineers ‘Outgrant’ application process

## Slide 6: Raw Water Intake and Pump Station

## Slide 7: Raw Water Pump Station
Will include structures and equipment to pump untreated water to the proposed water plant, located 15 miles north, as well as:
Vegetation Buffer Plans
The design will seek to minimize impacts on neighbors & will maintain/enhance vegetated buffers.
Deep ‘wet well’ that pumps will draw from, connected to lake intake by ¾-mile deep tunnel pipeline
Pipeline conveying raw water from pump station to Seaforth Rd
Lighting, parking, and fencing
Some carbon/chemical storage
Electrical power feed
Standby electrical generator

## Slide 8: Previous Seaforth property site plan
New plan hasn’t been developed yet for site’s modified role in the Water Supply Program
Design-Build Team to begin design work in June – site plan for Raw Water Pump station by fall
Durham will develop only a portion of the previously-proposed facilities
Construction focused on Pump Station and associated facilities in SE corner of property, plus water transmission pipeline crossing site

## Slide 9: Common Questions about Intake/Raw Water Facilities project
Schedule
Construction currently expected to start winter 2027 – centered in 2 areas
Water Pump Station site Vista Point Recreation Area
Tunnel Shaft (2027)
Tunnel (2027-2028) Lake Intake (2028-2029)
Pump Station (2028-2031)
Commissioning/Startup – Both Sites (2031-2032)
Traffic
During construction
Vista Point Recreation Area to be temporarily closed during Lake Intake construction, and area used for contractor’s staging.
Peak 50-100 construction staff
Concrete, materials, equipment, hauling away
Once Intake & Pump Station are operating
Limited number of staff – remote monitoring with regular checks; Intake not occupied
Deliveries, service vehicles infrequent (weekday, daytime)
Noise
Vegetated buffers help mitigate off-site noise
Specified dB limits on equipment that creates significant noise (ex: pump motors)
Pumps and emergency generators placed in buildings designed with sound attenuation
Noise study during design
Vibration during construction or operation – will be measurements, notifications as needed during construction
Lighting
Vegetated buffers help mitigate off-site noise
Design to use fixtures that limit up-lighting to the sky
Energy-efficient LED, sodium fixtures (warm color)
Provide only the necessary amount of lighting; use motion sensors, timers
Will comply with County ordinances on lighting

## Slide 10: Transmission Main Alignment

## Slide 11: WTP Preliminary Rendering
Preliminary Concept – other concepts being considered

## Slide 12: Community Commitment
City and WIP are committed to being good neighbor
  Sessions like today are part of how we live out the values of…
  Quality, Sustainability, Transparency, Equity, Partnership
We want to hear constructive ideas for building long-term, “good-neighbor” relationship
Notes: Transition back to Jeff for this slide and next.

## Slide 13: Communications
How to Submit a Comment
  Submit a comment on the website JordanLakeWaterSupply.com using the online comment form.
  Submit your comments in person today at our Community Open House.
  Mail a letter to 555 Fayetteville Street, Ste 900, Raleigh, NC 27601.
Comments will be accepted through the project design phase. As the project progresses, additional public meeting opportunities will be available.
You can sign up to join our stakeholder email list and receive quarterly newsletter updates on the project website: JordanLakeWaterSupply.com

## Slide 15: Raw Water Intake and Pump Station

## Slide 16: Transmission Main Construction
Construction will be in cleared corridors or adjacent to the right of way.
Restoration and temporary driveway repair will occur following pipe installation.
Easement width and location will vary along the pipe route.
After construction, the corridor is stabilized and grass is allowed to grow.

## Slide 17: What’s included in a typical water plant?
Employee & visitor parking
Administration offices
Laboratory
Maintenance shop
Electrical power supply
Emergency generators
Storage tanks (untreated & treated water)
Treatment basins & facilities
Chemicals to treat the water
Disinfection process
Treated water (“finished water”) pump station
Facility to thicken, store & haul away solids/sediments from treatment process
Roads, stormwater management
Space for future expansion
~10-20 employees typical
  Plant tours for student groups are common
2 entrances
Fencing & gates
Physical security (CCTV cameras, key-card access for gates & buildings)
Notes: Transition to Bill. Do not need to read the list – this is just list of what would be at a WTP.

## Slide 18: Chemicals and Odors
Preliminary list of chemicals:
    Coagulant (such as alum or ferric sulfate)
    Caustic and/or lime
    Polymer
    Sodium Hypochlorite for disinfection
    Fluoride
    Corrosion Inhibitor
    Ozone
    Permanganate
    Aqua Ammonia
    Calcium thiosulfate or bisulfite (for dechlorination)
Chemicals will be stored in accordance with City, County and State Building Codes
All chemicals will be liquid (except ozone, which is generated as needed, and possibly also a dry polymer) and stored in tanks in a building as in the photo
Most chemicals will be over 6,000 gallons stored so that chemicals can be purchased in truckloads so less trucking required
No detectable odors are expected offsite
Notes: There will be no chlorine gas used or stored at the site.

## Slide 19: Key Environmental Findings
Key findings from the environmental assessment include:
  No potential Environmental Justice concerns have been identified
  WIP will continue to gather community information and communicate with the public on its plans
  The JLWSP will satisfy important public supply water needs through 2070 and beyond
  Recreational uses at Vista Point Recreation Access Area to be suspended during part of the JLWSP construction period
  City of Durham is working with NC Parks to mitigate the temporary closure of this facility for ~ 3 years
  Placement of intake tower in Jordan Lake could pose potential safety concerns for boaters
  City of Durham is working with NC Wildlife Resource Commission to mitigate any concerns

## Slide 20: Key Environmental Findings
Key findings from the environmental assessment include:
  Little or no significant impact for most environmental resources
  No impacts to historic or archaeological features, with concurrence from the NC State Historic Preservation Office
  Most disturbances to wetlands, streams and surface waters will be temporary, and permanent impacts will be restricted to small areas
  No significant impacts to fish and aquatic wildlife
  No significant impacts to air quality, climate, floodplains, groundwater, wildlife, land use, traffic, hazardous materials
  Unavoidable loss of trees at the Pump Station site and Treatment Plant site, and along the transmission pipeline to Durham
  Pump Station Facility and Treatment Facility will have permanent forested buffer on all sides
  Pipeline corridor managed to control nuisance vegetation and trees will be allowed to regrow in parts of the corridor

## Slide 21: Welcome!
We’re glad you’re here
Primarily open house format, with some information to highlight in a presentation format
Please sign in if you did not already
Sign up for our newsletter and emails!
Q&A time
Same presentation at 6:30 & 7:15
Notes: Inga for this slide then Jeff will begin with the next.

## Slide 22: Our Approach
The City of Durham strives to continue providing reliable, high-quality drinking water to its customers.
The City’s Core Values for the Jordan Lake Water Supply Program are ...
Quality
Transparency
Public Engagement
Sustainability
Equity
Partnership
Our Approach
The overarching approach to addressing environmental resource concerns is to:
Identify resources with the potential for impact,
Avoid disturbance of resources wherever feasible,
Minimize disturbance when resource impacts cannot be avoided, and
Mitigate for unavoidable impacts.
Identify
Avoid
Minimize
Mitigate